## Slide 1: IFTC 211- digital logic design
Data Representation & Numbering Systems

## Slide 2: module 1
Data Representation & Numbering Systems

## Slide 3: Data Representation & Numbering Systems
Outline:
Definition of data.
Examples of data in various forms.
Importance of data representation in computing.
Binary Numbering Systems
Octal Numbering Systems
Decimal Numbering Systems
Hexadecimal Numbering Systems

## Slide 4: Data Representation & Numbering Systems
Specific Objectives:
By the end of this module, you should be able:
Explain why everything is data in computers.
Understand the importance of data representation.
Describe Number Systems (Binary, Octal, Decimal and Hexadecimal)
To convert from one number system to another

## Slide 5: Data Representation & Numbering Systems
Data is any collection of raw facts and figures, which can be processed to extract meaningful information.
Data refers to any collection of raw facts and figures that can be processed by a computer to extract meaningful information. It includes numbers, characters, images, and sounds.
Types of Data:
  Numeric Data: Integers, floating-point numbers.
  Alphanumeric Data: Characters, strings.
  Multimedia Data: Images, audio, video.
Data in Computing: In computers, everything from instructions to multimedia content is represented as data.

## Slide 6: Numbering Systems
Most modern computer systems do not represent numeric values using the decimal numbering system. They use the binary or two’s complement numbering system.
But when dealing with a computer at the machine level, we must be more concerned with how data are stored.
Hence the job of converting data from one representation to another must be carried out.
The important number systems are
  decimal, base ten (B10).
  binary, base two (B2).
  octal, base eight (B8).
  hexadecimal, base sixteen (B16).
It is often required to convert a number in a particular number system to any other number system, e.g. it may be required to convert a decimal number to binary or octal or hexadecimal. The reverse is also true, i.e., a binary number may be converted into decimal and so on.

## Slide 7: Numbering Systems
Importance of Data Representation: Accurate data representation is crucial for efficient data processing, storage, and retrieval.
Efficiency: Proper data representation can optimize the speed and efficiency of data processing.
Storage: Efficient data representation saves storage space and allows for faster retrieval.
Accuracy: Accurate data representation minimizes errors during data processing and transmission.
Examples:
Text data (ASCII, Unicode).
Image data (Bitmap, JPEG).
Sound data (WAV, MP3).

## Slide 8: Decimal Number System Representation (B10)
Most people today use decimal representation to count. In the decimal system there are 10 digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
These digits can be used to represent any value, for example: 754.
The value is formed by the sum of each digit, multiplied by the base (in this case it is 10 because there are 10 digits in decimal system) in power of digit position (counting from zero).
7x102 + 5x101 + 4x100
= 7x100 + 5x10 + 4x1
= 700 + 50 + 4
= 754

## Slide 9: Binary Number System Representation (B2)
The computer represents values using two voltage levels (usually 0v and +5v).
These two values, coincidentally, correspond to the two digits used by the binary numbering system.
Each digit in a binary number is called a BIT, 4 bits form a NIBBLE, 8 bits form a BYTE, two bytes form a WORD, and two words form a DOUBLE WORD (rarely used).
Counting binary numbers must be from right, Least Significant Bit (LSB) to left, Most Significant Bit (MSB).

## Slide 10: Binary Number System Representation (B2)
10111100102 is equivalent to 75410
1x29 + 0x28 + 1x27 + 1x26 + 1x25 + 1x24 + 0x23 + 0x22 + 1x21 + 0x20
= 1x512 + 0x256 + 1x128 + 1x64 +1x32 + 1x16 + 0x8 + 0x4 +1x2 +0x1
= 512 + 0 + 128 + 64 + 32 + 16 + 0 + 0 + 2 + 0
= 754
Hence:
The binary number 1011110010b equals to decimal value of 754 as can be seen above.
There is a convention to add "b“ or “B” in the end of a binary number, this way we can determine that 1011110010b is a binary number with decimal value of 754.

## Slide 11: Octal Number System Representation (B8)
Octal number system uses 8 values (0, 1, 2, 3, 4, 5, 6, 7) to represent numbers with 0 having the least value and 7 having the greatest value.
Octal number system was used extensively in the early mainframe computer systems but has become less popular in favour of binary and hexadecimal.
For example:
The figure, 778 has the first symbol, '7' on the right hand side carrying a multiplying factor of 80 and the second symbol, '7' from the left hand side carrying a multiplying factor of 81.
This figures can then be expressed as:
----------------------------------------778 = 7x81 + 7x80 = 6310

## Slide 12: Octal Number System Representation (B8)
Another example of octal number system is:
Using the positional value of each octal digit, we can easily convert octal integer numbers to decimal.
E.g.: (171)8 = 1 x 82 + 7 x 81 + 1 x 80
= 64 + 56 + 1 = 121
(171)8 = (121)10
The digits that belong to the octal number system can be easily converted to the binary system to give the table below:
Octal (base 8) numbers must have "q or o" suffix, example: 77o or 77q.

## Slide 13: Hexadecimal Number System Representation (B16)
Hexadecimal number system uses base 16. The digits in this system range from 0 to 15. By convention, the letters A through F is used to represent the hexadecimal digits corresponding to decimal values 10 through 15.
Hexadecimal digits are: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F .
Hexadecimal numbers in computing is used for abbreviating lengthy binary representations.
Hexadecimal numbers are compact and easy to read, hence used often in bigger machines.
It is very easy to convert numbers from binary system to hexadecimal system and vice-versa.
There is a convention to add "h" in the end of a hexadecimal number, this way we can determine that the assigned value is a hexadecimal number.
"0" (zero) is also added in the beginning of hexadecimal numbers that begin with a letter (A..F), to avoid ambiguity.

## Slide 14: Converting from Decimal System to Other Number System
In order to convert from decimal system, to any other system:
  It is required to divide the decimal value by the base of the desired system
  Remember the result and keep the remainder
  Divide process continues until the result is zero
  Then the column of the remainder is read in reverse order i.e., from bottom to top order.
  The remainders are then used to represent a value in that system.
Example 1: The conversion of the value of 75 (base 10) to Octal System (base 8) can be seen below:
(75)10 converted to octal will give:
75 ÷ 8 = 9 remainder 3
9 ÷ 8 = 1 remainder 1
1 ÷ 8 = 0 remainder 1
Therefore; (75)10 = (113)8

## Slide 15: Converting from Decimal System to Other Number Systems
Example2: Convert 75 (base 10) to base 2.
75 converted to binary will give:
75 ÷ 2 = 37 remainder 1
37 ÷ 2 = 18 remainder 1
18 ÷ 2 = 9 remainder 0
9 ÷ 2 = 4 remainder 1
4 ÷ 2 = 2 remainder 0
2 ÷ 2 = 1 remainder 0
1 ÷ 2 = 0 remainder 1
Therefore, (75)10 = (1001011)2
Example 3: Convert 34810 into a hexadecimal number.
Solution.
348/16 = 21 remainder 12
21/16 = 1 remainder 5
1/16 = 0 remainder 1
Hence the converted hexadecimal number is 15C16. or 15Ch

## Slide 16: Converting from Other Number Systems to Decimal System
Example1: Convert 101102 into a decimal number.
Solution:
1*24 + 0*23 + 1*22 + 1*21 + 0*20
= 16 + 0 + 4 + 2 + 0
= 2210
Example2: Convert 34628 into a decimal number.
Solution:
3*83 + 4*82 + 6*81 + 2*80
= 1536 + 256 + 48 + 2
= 184210
Example 3: Convert 42AD16 into a decimal number.
Solution:
4*163 + 2*162 + 10*161 + 13*160
= 16384 + 512 + 160 + 13
= 1706910
The method of conversion of binary, octal, or hexadecimal numbers to decimal numbers is illustrated in the examples below:

## Slide 17: Conversion from a Binary to Octal Number and Vice Versa
We know that the maximum digit in an octal number system is 7, which can be represented as 1112 in a binary system. Hence, starting from the LSB, we group three digits at a time and replace them by the decimal equivalent of those groups and we get the final octal number.
Example 1: Convert 1011010102 into an equivalent octal number.
Solution.
The binary number given as 101101010
Starting with LSB and grouping 3 bits:
101 101 010
Octal equivalent 5 5 2
Hence the octal equivalent number is (552)8.
Now if the octal number is given and you're asked to convert it into its binary equivalent, then each octal digit is converted into a 3-bit-equivalent binary number and - combining all those digits we get the final binary equivalent.
Example 2: Convert 2358 into an equivalent binary number.
Solution.
The octal number given as 2 3 5
3-bit binary equivalent 010 011 101
Hence the binary number is (010011101)2.
NOTE: When converting from binary and the last group cannot be completed during grouping of the three digits starting from the LSB, then we complete the group by adding 0s in the MSB side. This is called left padding of the number with 0.

## Slide 18: Conversion from a Binary to Hexadecimal Number and Vice Versa
We know that the maximum digit in a hexadecimal system is 15, which can be represented by 11112 in a binary system. Hence, starting from the LSB, we group four digits at a time and replace them with the hexadecimal equivalent of those groups and we get the final hexadecimal number.
Example 1: Convert 110101102 into an equivalent hexadecimal number.
Solution.
The binary number given as 11010110
Starting with LSB and grouping 4 bits 1101 0110
Hexadecimal equivalent D 6
Hence the hexadecimal equivalent number is (D6)16.
Now if the hexadecimal number is given and you're asked to convert it into its binary equivalent, then each hexadecimal digit is converted into a 4-bit-equivalent binary number and by combining all those digits we get the final binary equivalent.
Example 1: Convert 29C16 into an equivalent binary number.
Solution.
The hexadecimal number given as 2 9 C
4-bit binary equivalent 0010 1001 1100
Hence the equivalent binary number is (001010011100)2.
NOTE: When converting from binary and the last group cannot be completed during grouping of the four digits starting from the LSB, then we complete the group by adding 0s in the MSB side. This is called left padding of the number with 0.

## Slide 19: Conversion from an Octal to Hexadecimal Number and Vice Versa
Conversion from octal to hexadecimal and vice versa is sometimes required.
To convert an octal number into a hexadecimal number the following steps are to be followed:
  i. First convert the octal number to its binary equivalent
  ii. Then form groups of 4 bits, starting from the LSB.
  iii. Then write the equivalent hexadecimal number for each group of 4 bits.
Similarly, for converting a hexadecimal number into an octal number the following steps are to be followed:
  i. First convert the hexadecimal number to its binary equivalent.
  ii. Then form groups of 3 bits, starting from the LSB.
  iii. Then write the equivalent octal number for each group of 3 bits.

## Slide 20: Conversion from an Octal to Hexadecimal Number and Vice Versa
Example 1: Convert hexadecimal number A72E into octal number equivalent.
Solution.
Given hexadecimal number as: A 7 2 E
Binary equivalent is 1010 0111 0010 1110
= 1010011100101110
Forming groups of 3 bits from the LSB, we have 001 010 011 100 101 110
Octal equivalent is 1 2 3 4 5 6
Hence the octal equivalent of (A72E)16 is (123456)8.
Example 1.24. Convert (247)8 into an equivalent hexadecimal number.
Solution.
Given octal number is 2 4 7
Binary equivalent is 010 100 111
= 010100111
Forming groups of 4 bits from the LSB 1010 0111
Hexadecimal equivalent is A 7
Hence the hexadecimal equivalent of (247)8 is (A7)16.

## Slide 21: Counting from 0 to 16 In Binary Prefix Notations
In Binary | In Decimal | In Hex Decimal | In Octal
0000 | 0 | 0 | 0
0001 | 1 | 1 | 1
0010 | 2 | 2 | 2
0011 | 3 | 3 | 3
0100 | 4 | 4 | 4
0101 | 5 | 5 | 5
0110 | 6 | 6 | 6
0111 | 7 | 7 | 7
1000 | 8 | 8 | 10
1001 | 9 | 9 | 11
1010 | 10 | A | 12
1011 | 11 | B | 13
1100 | 12 | C | 14
1101 | 13 | D | 15
1110 | 14 | E | 16
1111 | 15 | F | 17

## Slide 22: ASSIGNMENT
Fill the table below:
S/N | BINARY | OCTAL | DECIMAL | HEXADECIMAL
1 |  | 3462q |  | 
2 |  |  |  | 42ADh
3 | 110011110b |  |  |